Stratix® V GX, GS and E Device Schematic Review Worksheet

This document is intended to help you review your schematic and compare the pin usage against the Stratix V E, GS, and GX Device Family Pin Connection Guidelines (PDF) version 1.6 and other referenced literature for this device family.  The technical content is divided into focus areas such as FPGA power supplies, transceiver power supplies and pin usage, configuration, and FPGA I/O, and external memory interfaces.

Within each focus area, there is a table that contains the voltage or pin name for all of the dedicated and dual purpose pins for the device family.  In some cases, the device density and package combination may not include some of the pins shown in this worksheet, you should cross reference with the pin-out file for your specific device.  Links to the device pin-out files are provided at the top of each section.

Before you begin using this worksheet to review your schematic and commit to board layout, Altera highly recommends:

1) Review the latest version of the Stratix V Errata Sheet (PDF) and the Knowledge Database for Stratix V Device Known Issues and Stratix V Device Handbook Known Issues.

2)  Compile your design in the Quartus® II software to completion.

For example, there are many I/O related placement restrictions and VCCIO requirements for the I/O standards used in the device.  If you do not have a complete project, then at a minimum a top level project should be used with all I/O pins defined, placed, and apply all of the configurable options that you plan to use.  All I/O related megafunctions should also be included in the minimal project, including, but not limited to, external memory interfaces, transceiver IP, PLLs, altlvds, and altddio.  The I/O Analysis tool in the Pin Planner can then be used on the minimal project to validate the pinout in the Quartus II software to assure there are no conflicts with the device rules and guidelines.

When using the I/O Analysis tool you must ensure there are no errors with your pinout.  Additionally, you should check all warning and critical warning messages to evaluate their impact on your design.  You can right click your mouse over any warning or critical warning message and select “Help”.  This will bring open a new Help window with further information on the cause of the warning, and the action that is required.

For example, the following warning is generated when a PLL is driven by a global network where the source is a valid dedicated clock input pin, but the pin is not one dedicated to the particular PLL:

Warning: PLL "<PLL Instance Name>" input clock inclk[0] is not fully compensated and may have reduced jitter performance because it is fed by a non-dedicated input

Info: Input port INCLK[0] of node "<PLL Instance Name>" is driven by clock~clkctrl which is OUTCLK output port of Clock Control Block type node clock~clkctrl

The help file provides the following:

| CAUSE: | The specified PLL's input clock is not driven by a dedicated input pin. As a result, the input clock delay will not be fully compensated by the PLL. Additionally, jitter performance depends on the switching rate of other design elements. This can also occur if a global signal assignment is applied to the clock input pin, which forces the clock to use the non-dedicated global clock network. |
| --- | --- |
| ACTION: | If you want compensation of the specified input clock or better jitter performance, connect the input clock only to an input pin, or assign the input pin only to a dedicated input clock location for the PLL. If you do not want compensation of the specified input clock, then set the PLL to No Compensation mode. |

When assigning the input pin to the proper dedicated clock pin location, refer to Clock Networks and PLLs in Stratix V Devices (PDF) for the proper port mapping of dedicated clock input pins to PLLs.

There are many reports available for use after a successful compilation or I/O analysis.  For example, you can use the “All Package Pins” and “I/O Bank Usage” reports within the Compilation – Fitter – Resource Section to see all of the I/O standards and I/O configurable options that are assigned to all of the pins in your design, as well as view the required VCCIO for each I/O bank.  These reports must match your schematic pin connections.

The review table has the following heading:

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |

The first column (Plane/Signal) lists the FPGA voltage or signal pin name.  You should only edit this column to remove dedicated or dual purpose pin names that are not available for your device density and package option.

The second column (Schematic Name) is for you to enter your schematic name(s) for the signal(s) or plane connected to the FPGA pin(s).

The third column (Connection Guidelines) should be considered “read only” as this contains Altera’s recommended connection guidelines for the voltage plane or signal.

The fourth column (Comments/Issues) is an area provided as a “notepad” for you to comment on any deviations from the connection guidelines, and to verify guidelines are met.  In many cases there are notes that provide further information and detail that compliment the connection guidelines.

Here is an example of how the worksheet can be used:

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| <Plane / Signal name provided by Altera> VCC | <user entered text> +0.85V | <Device Specific Guidelines provided by Altera> | <user entered text> Connected to +0.85V plane, no isolation is necessary. Missing low and medium range decoupling, check PDN. See Notes (1-1) (1-2). |

Legal Note:

PLEASE REVIEW THE FOLLOWING TERMS AND CONDITIONS CAREFULLY BEFORE USING THIS SCHEMATIC REVIEW WORKSHEET (“WORKSHEET”) PROVIDED TO YOU. BY USING THIS WORKSHEET, YOU INDICATE YOUR ACCEPTANCE OF SUCH TERMS AND CONDITIONS, WHICH CONSTITUTE THE LICENSE AGREEMENT ("AGREEMENT") BETWEEN YOU AND ALTERA CORPORATION OR ITS APPLICABLE SUBSIDIARIES ("ALTERA").

1. Subject to the terms and conditions of this Agreement, Altera grants to you, for no additional fee, a non-exclusive and non-transferable right to use this Worksheet for the sole purpose of verifying the validity of the pin connections of an Altera programmable logic device-based design. You may not use this Worksheet for any other purpose.  There are no implied licenses granted under this Agreement, and all rights, except for those granted under this Agreement, remain with Altera.

2. Altera does not guarantee or imply the reliability, or serviceability, of this Worksheet or other items provided as part of this Worksheet. This Worksheet is provided 'AS IS'. ALTERA DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, INCLUDING THE IMPLIED WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, AND NON-INFRINGEMENT.  ALTERA HAS NO OBLIGATION TO PROVIDE YOU WITH ANY SUPPORT OR MAINTENANCE.

3. In no event shall the aggregate liability of Altera relating to this Agreement or the subject matter hereof under any legal theory (whether in tort, contract, or otherwise), exceed One Hundred US Dollars (US$100.00). In no event shall Altera be liable for any lost revenue, lost profits, or other consequential, indirect, or special damages caused by your use of this Worksheet even if advised of the possibility of such damages.

4. This Agreement may be terminated by either party for any reason at any time upon 30-days’ prior written notice.  This Agreement shall be governed by the laws of the State of California, without regard to conflict of law or choice of law principles. You agree to submit to the exclusive jurisdiction of the courts in the County of Santa Clara, State of California for the resolution of any dispute or claim arising out of or relating to this Agreement. The parties hereby agree that the party who is not the substantially prevailing party with respect to a dispute, claim, or controversy relating to this Agreement shall pay the costs actually incurred by the substantially prevailing party in relation to such dispute, claim, or controversy, including attorneys' fees.  Failure to enforce any term or condition of this Agreement shall not be deemed a waiver of the right to later enforce such term or condition or any other term or condition of the Agreement.

BY USING THIS WORKSHEET, YOU ACKNOWLEDGE THAT YOU HAVE READ THIS AGREEMENT, UNDERSTAND IT, AND AGREE TO BE BOUND BY ITS TERMS AND CONDITIONS. YOU AND ALTERA FURTHER AGREE THAT IT IS THE COMPLETE AND EXCLUSIVE STATEMENT OF THE AGREEMENT BETWEEN YOU AND ALTERA, WHICH SUPERSEDES ANY PROPOSAL OR PRIOR AGREEMENT, ORAL OR WRITTEN, AND ANY OTHER COMMUNICATIONS BETWEEN YOU AND ALTERA RELATING TO THE SUBJECT MATTER OF THIS AGREEMENT.

Index

Section I: 	Power

Section II: 	Configuration

Section III: 	Transceiver

Section IV: 	I/O

a:	Clock Pins

b:	Dedicated and Dual Purpose Pins

c: 	Dual Purpose Differential I/O pins

Section V: 	External Memory Interface Pins

a:	DDR/2 Interface Pins

b: 	DDR/2 Termination Guidelines

c: 	DDR3 Interface Pins

d: 	DDR3 Termination Guidelines

e:	QDRII/+ Interface pins

f:	QDRII/+ Termination Guidelines

g: 	RLDRAMII/3 Interface Pins

h: 	RLDRAMII/3 Termination Guidelines

Section VI:	Document Revision History

Section I: Power

Documentation: Stratix V Devices

Stratix V Pin Out Files

Stratix V E, GS, GX Device Family Pin Connection Guidelines (PDF)

Stratix V Early Power Estimator

Stratix V Early Power Estimator User Guide (PDF)

Power Delivery Network (PDN) Tool For Stratix V Devices

Device-Specific Power Delivery Network (PDN) Tool User Guide (PDF)

PowerPlay Power Analyzer Support Resources

Altera Board Design Resource Center (General board design guidelines, PDN design, isolation, tools, and more)

AN 583: Designing Power Isolation Filters with Ferrite Beads for Altera FPGAs (PDF)

AN 597: Getting Started Flow for Board Designs (PDF)

Errata Sheet and Guidelines for Stratix V ES Devices (PDF)

Errata Sheet for Stratix V Devices (PDF)

Known Stratix V Issues

Index

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCC |  | For -1 and -2 speed grades, connect all VCC pins to a 0.9V low noise switching regulator. For -3 and -4 speed grades, connect all VCC pins to a 0.85V low noise switching regulator. When VCCHIP and VCCHSSI are used, they must be tied to the same plane as VCC. For data rates less than 6.5Gbps and with a proper isolation filter VCCR_GXB and VCCT_GXB may be sourced from the same regulator as VCC when the power rails require the same voltage level. All Stratix V power pins that can be shared with VCC can be connected to 0.9V or 0.85V depending on the speed grade of the device. Use the Stratix V Early Power Estimator to determine the current requirements for VCC and other supplies. These supplies may share power planes across multiple Stratix V devices. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-3) (1-4). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCIO[3,4,7,8] [A,B,C,D,E] (not all pins are available in each device / package combination) |  | Connect these pin to 1.2V, 1.25V, 1.35V, 1.5V, 1.8V, 2.5V or 3.0V supplies, depending on the I/O standard connected to the specified bank. When these pins require the same voltage level as VCCPD and / or VCCPGM, they may be tied to the same regulator as VCCPD and / or VCCPGM. These supplies may share power planes across multiple Stratix V devices. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCPD3AB VCCPD3CD VCCPD[4,7,8] (not all pins are available in each device / package combination) |  | The VCCPD pins require 2.5V or 3.0V. VCCPD voltage connection depends on the VCCIO voltage of the bank. VCCIO3E if supported by the device uses VCCPD3CD. VCCPD for 3.0V VCCIO is 3.0V, VCCPD for 2.5V/1.8V/1.5V/1.35V/1.25V/1.2V VCCIO is 2.5V. When these pins require the same voltage level as VCCIO and / or VCCPGM, they may be tied to the same regulator as VCCIO and / or VCCPGM. These supplies may share power planes across multiple Stratix V devices. For 3.0V operation, refer to VCCPD Restrictions in I/O Features in Stratix V Devices (PDF) for further information. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCPGM |  | Connect these pins to either 1.8V, 2.5V or 3.0V. When these pins require the same voltage level as VCCPD and / or VCCIO, they may be tied to the same regulator as VCCPD and / or VCCIO. These supplies may share power planes across multiple Stratix V devices. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VREF[3,4,7,8] [A,B,C,D,E]N0 (not all pins are available in each device / package combination) |  | Input reference voltage for each I/O bank. If a bank uses a voltage referenced I/O standard, then these pins are used as the voltage-reference pins for the I/O bank. If VREF pins are not used, you should connect them to either the VCCIO in the bank where the pin resides or GND. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCBAT |  | Connect this pin to a non-volatile battery power source in the range of 1.2V – 3.0V when using the design security volatile key. In this case, do not connect this pin to a volatile power source on the board. 3.0V is the typical power selected for this supply. When not using the volatile key, tie this to a 1.5V, 2.5V, or 3.0V supply. If using 1.5V, this pin may be tied to the same regulator as VCCPT, VCCD_FPLL, and VCCH_GXB. Stratix V devices will not exit POR if VCCBAT stays at logic low. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCPT |  | Connect all VCCPT pins to a 1.5V linear or low noise switching power supply. These pins may be tied to the same regulator as VCCD_FPLL, VCCBAT, and VCCH_GXB. These supplies can share planes across multiple Stratix V devices. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-3). |
| VCCD_FPLL |  | Connect all VCCD_FPLL pins to a 1.5V linear or low noise switching power supply. These pins may be tied to the same regulator as VCCPT, VCCBAT, and VCCH_GXB. These supplies may share power planes across multiple Stratix V devices. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCAUX |  | Connect all VCCAUX pins to a 2.5V low noise switching power supply through a proper isolation filter. This power rail may be shared with VCCA_FPLL. With a proper isolation filter these pins may be sourced from the same regulator as VCCIO, VCCPD, and VCCPGM when each of these power supplies require 2.5V. These supplies may share power planes across multiple Stratix V devices. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-3) (1-4). |
| VCCA_FPLL |  | Connect these pins to a 2.5V low noise switching power supply through a proper isolation filter. This power rail may be shared with VCCAUX. With a proper isolation filter these pins may be sourced from the same regulator as VCCIO, VCCPD, and VCCPGM when each of these supplies require 2.5V. These supplies may share power planes across multiple Stratix V devices. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2) (1-3). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| RREF_[T,B][L,R] |  | If any PLLs are used in the device, you must ensure the proper RREF_[T,B][L,R] pins are connected to their own individual 1.8-kΩ +/- 1% resistor to GND (see transceiver section of this review for further details on the requirements for this pin). | Verify Guidelines have been met or list required actions for compliance. |
| GND |  | All GND pins must be connected to the board ground plane. | Verify Guidelines have been met or list required actions for compliance. See Notes (1-1) (1-2). |

Index  Top of Section

Notes:

1-1. This worksheet does not calculate required decoupling, it is expected the designer will select decoupling based on analysis of power required and impedance of power path required based on static and switching current values.  Refer to Altera’s Power Delivery Network (PDN) Tool for Stratix V Devices for further information.

Capacitance values for the power supply should be selected after consideration of the amount of power they need to supply over the frequency of operation of the particular circuit being decoupled. A target impedance for the power plane should be calculated based on current draw and voltage drop requirements of the device/supply. The power plane should then be decoupled using the appropriate number of capacitors. On-board capacitors do not decouple higher than 100 MHz due to “Equivalent Series Inductance” of the mounting of the packages. Proper board design techniques such as interplane capacitance with low inductance should be considered for higher frequency decoupling.

1-2. This worksheet does not include power estimation for the different power supplies provided. Ensure each power supply is adequate for the device current requirements.  Refer to Altera’s Early Power Estimation Tools and PowerPlay Power Analyzer Support Resources for further guidance.

Use Altera’s Early Power Estimation Tools to ensure the junction temperature of the device is within operating specifications based on your design activity.

1-3. Low Noise Switching Regulator is defined as a switching regulator circuit encapsulated in a thin surface mount package containing the switch controller, power FETs, inductor, and other support components.  The switching frequency is usually between 800kHz and 1MHz and has a fast transient response.  The switching range is not an Altera requirement.  However, Altera does require the Line Regulation and Load Regulation meet the following specifications:

Line Regulation < 0.4%.

Load Regulation < 1.2%

1-4. Power pins should not share breakout vias from the BGA.  Each ball on the BGA needs to have its own dedicated breakout via.  VCC must not share breakout vias.

Index  Top of Section

Reviewed against Errata Sheet for Stratix V Devices (PDF) version:

Additional Comments:

Index  Top of Section

Section II: Configuration

Stratix V Recommended Reference Literature/Tool List

Stratix V Pin Out Files

Stratix V E, GS, GX Device Family Pin Connection Guidelines (PDF)

Configuration, Design Security, and Remote System Upgrades in Stratix V Devices (PDF)

JTAG Boundary-Scan Testing in Stratix V Devices (PDF)

USB-Blaster Download Cable User Guide (PDF)

ByteBlaster II Download Cable User Guide (PDF)

EthernetBlaster II Communications Cable User Guide (PDF)

AN 597: Getting Started Flow for Board Designs (PDF)

Errata Sheet and Guidelines for Stratix V ES Devices (PDF)

Errata Sheet for Stratix V Devices (PDF)

Index

| Configuration Scheme | Configuration Voltage |  |
| --- | --- | --- |

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| nIO_PULLUP |  | Dedicated input to enable the internal pull-up resistors on the user I/O pins and dual-purpose I/O pins (DATA[0:31], CLKUSR, INIT_DONE, DEV_OE, DEV_CLRn) before and during configuration. A logic low turns on these internal pull-up resistors. The nIO_PULLUP pin must be tied to GND. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| MSEL[0:4] |  | These pins are internally connected through a 25-kΩ resistor to GND. Do not leave these pins floating. When these pins are unused connect them to GND. Depending on the configuration scheme used these pins should be tied to VCCPGM or GND. Refer to Configuration, Design Security, and Remote System Upgrades in Stratix V Devices (PDF) for the configuration scheme options. If only JTAG configuration is used, connect these pins to ground. | Verify Guidelines have been met or list required actions for compliance. |
| nCE |  | Dedicated active-low chip enable. When nCE is low, the device is enabled. When nCE is high, the device is disabled. In multi-device configuration, nCE of the first device is tied low while its nCEO pin drives the nCE of the next device in the chain. In single device configuration and JTAG programming, nCE should be connected to GND or through a 10-kΩ pull-down to GND if using an Active Serial header. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| nCONFIG |  | Dedicated configuration control input. Pulling this pin low during user-mode will cause the FPGA to lose its configuration data, enter a reset state, and tri-state all I/O pins. Returning this pin to a logic high level will initiate reconfiguration. nCONFIG should be connected directly to the configuration controller when the FPGA uses a passive configuration scheme, or through a 10-kΩ resistor tied to VCCPGM when using an active serial configuration scheme. If this pin is not used, it requires a connection directly or through a 10-kΩ resistor to VCCPGM. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| CONF_DONE |  | This is a dedicated configuration done pin. As a status output, the CONF_DONE pin drives low before and during configuration. Once all configuration data is received without error and the initialization cycle starts, CONF_DONE is released. As a status input, CONF_DONE goes high after all data is received. Then the device initializes and enters user mode. It is not available as a user I/O pin. If internal pull-up resistors on the configuration controller or enhanced configuration device are used, external 10-kΩ pull-up resistors should not be used on this pin. Otherwise, use an external 10-kΩ pull-up resistor to VCCPGM should be used. When using passive configuration schemes this pin should also be monitored by the configuration controller. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| nCEO |  | During multi-device configuration, this pin feeds the nCE pin of a subsequent device. Connect this pin to an external 10-kΩ pull-up resistor to VCCPGM. During single device configuration, this pin may be left floating. This pin is not available for regular I/O usage in multi-device configuration mode, see rd04132011_29. | Verify Guidelines have been met or list required actions for compliance. |
| nSTATUS |  | This is a dedicated configuration status pin. The FPGA drives nSTATUS low immediately after power-up and releases it after POR time. As a status output, the nSTATUS is pulled low if an error occurs during configuration. As a status input, the device enters an error state when nSTATUS is driven low by an external source during configuration or initialization. It is not available as a user I/O pin. The OE and nCE pins of the enhanced configuration devices have optional internal programmable pull-up resistors. If internal pull-up resistors on the enhanced configuration device are used, external 10-kΩ pull-up should not be used on these pins. Otherwise, an external 10-kΩ pull-up resistors to VCCPGM should be used. When using Passive configuration schemes this pin should also be monitored by the configuration controller. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| TCK |  | Connect this pin to a 1-kΩ pull-down resistor to GND. This pin has an internal 25-kΩ pull-down. Treat this signal like a clock and follow typical clock routing guidelines. | Verify Guidelines have been met or list required actions for compliance. |
| TMS |  | Connect this pin to a 1-kΩ - 10-kΩ pull-up resistor to VCCPD. To disable the JTAG circuitry connect TMS to VCCPD via a 1- kΩ resistor. This pin has an internal 25-kΩ pull-up. | Verify Guidelines have been met or list required actions for compliance. |
| TDI |  | Connect this pin to a 1-kΩ - 10-kΩ pull-up resistor to VCCPD. To disable the JTAG circuitry connect TDI to VCCPD via a 1- kΩ resistor. This pin has an internal 25-kΩ pull-up. | Verify Guidelines have been met or list required actions for compliance. |
| TDO |  | The JTAG circuitry can be disabled by leaving TDO unconnected. In cases where TDO uses VCCPD = 2.5 V to drive a 3.3V JTAG interface, there may be leakage current in the TDI input buffer of the interfacing devices. An external pull-up resistor tied to 3.3 V on their TDI pin may be used to eliminate the leakage current if needed. | Verify Guidelines have been met or list required actions for compliance. |
| TRST |  | Dedicated active low JTAG input pin. TRST is used to asynchronously reset the JTAG boundary-scan circuit. Utilization of TRST is optional. When using this pin ensure that TMS is held high or TCK is static when TRST is changed from low to high. If not using TRST, tie this pin to a 1-kΩ pull-up resistor to VCCPD. To disable the JTAG circuitry, tie this pin to GND. This pin has an internal 25-kΩ pull-up. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Optional Dual Purpose Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| nCSO |  | Dedicated output control signal from the FPGA to the serial configuration device in AS mode that enables the configuration device. When not programming the device in AS mode nCSO is not used. Also, when this pin is not used as an output then it is recommended to leave the pin unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| DCLK |  | Dedicated configuration clock pin. In PS and FPP configuration, DCLK is used to clock configuration data from an external source into the FPGA. In AS mode, DCLK is an output from the FPGA that provides timing for the configuration interface. Do not leave this pin floating. Drive this pin either high or low. | Verify Guidelines have been met or list required actions for compliance. |
| CRC_ERROR |  | This pin is optional and is used when the CRC error detection circuit is enabled. When using as optionally open-drain output dedicated CRC_ERROR pin, connect this pin to an external 10-kΩ pull-up resistor to VCCPGM. When not using as the dedicated CRC_ERROR pin, and when not using as a user I/O, connect this pin as defined in the Quartus II software. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| External Memory Interface Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| AS_DATA0 / ASDO |  | Dedicated AS configuration pin. When using an EPCS device (x1 mode) this is the ASDO pin and used to send address and control signals between the FPGA and the EPCS/EPCQ. When not programming the device in AS mode ASDO is not used. Also, when this pin is not used it is recommended to leave the pin unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| AS_DATA[1:3] |  | Dedicated AS configuration data pins. Configuration data is transported on these pins when connected to the EPCQ devices. When this pin is not used it is recommended to leave the pin unconnected. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Partial Reconfiguration Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| PR_REQUEST |  | Partial Reconfiguration Request pin. Drive this pin high to start partial reconfiguration. Drive this pin low to end reconfiguration. This pin can only be used in Partial Reconfiguration using external host mode in FPP x16 configuration scheme. When the dedicated input PR_REQUEST is not used and this pin is not used as an I/O, then it is recommended to tie this pin to GND. | Verify Guidelines have been met or list required actions for compliance. |
| PR_READY |  | When using as optionally open-drain output dedicated PR_READY pin, connect this pin to an external 10-kΩ pull-up resistor to VCCPGM. When not using as the dedicated PR_READY optionally open-drain output, and when this pin is not used as an I/O pin, then connect this pin as defined in the Quartus II software. | Verify Guidelines have been met or list required actions for compliance. |
| PR_ERROR |  | When using as optionally open-drain output dedicated PR_ERROR pin, connect this pin to an external 10-kΩ pull-up resistor to VCCPGM. When not using as the dedicated PR_ERROR optionally open-drain output, and when this pin is not used as an I/O pin, then connect this pin as defined in the Quartus II software. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| PR_DONE |  | When using as optionally open-drain output dedicated PR_DONE pin, connect this pin to an external 10-kΩ pull-up resistor to VCCPGM. When not using as the dedicated PR_DONE optionally open-drain output, and when this pin is not used as an I/O pin, then connect this pin as defined in the Quartus II software. | Verify Guidelines have been met or list required actions for compliance. |
| CvP_CONFDONE (N/A in Stratix V E Devices) |  | When using as optionally open-drain output dedicated CvP_CONFDONE pin, connect this pin to an external 10-kΩ pullup resistor to VCCPGM. When not using as the dedicated CvP_CONFDONE optionally open-drain output, and when this pin is not used as an I/O pin, then connect this pin as defined in the Quartus II software. |  |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DEV_CLRn |  | This pin is optional and allows you to override all clears on all device registers. When the dedicated input DEV_CLRn is not used and this pin is not used as an I/O then it is recommended to tie this pin to ground. | Verify Guidelines have been met or list required actions for compliance. |
| DEV_OE |  | This pin is optional and allows you to override all tri-states on the device. When the dedicated input DEV_OE is not used and this pin is not used as an I/O then it is recommended to tie this pin to ground. | Verify Guidelines have been met or list required actions for compliance. |
| DATA0 |  | Dual-purpose configuration data input pin. The DATA0 pin can be used for PS or FPP configuration or as an I/O pin after configuration is complete. When the dedicated input for DATA[0] is not used and this pin is not used as an I/O then it is recommended to leave this pin unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| DATA[1:31] |  | Dual-purpose configuration input data pins and user I/O pins after configuration. For FPP x8 use DATA[1:7] For FPP x16 use DATA[1:15] For FPP x32 use DATA[1:31] When the dedicated inputs for DATA[1:31] are not used and these pins are not used as an I/O then it is recommended to leave these pins unconnected. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| INIT_DONE |  | This is a dual-purpose pin and can be used as an I/O pin when not enabled as INIT_DONE. When using as optionally open-drain output dedicated INIT_DONE pin, a transition from low to high at the pin indicates when the device has entered user mode. The INIT_DONE pin cannot be used as a user I/O pin after configuration. Connect this pin to an external 10-kΩ pull-up resistor to VCCPGM. When using in an AS or PS multi-device configuration mode ensure INIT_DONE is enabled in the Quartus II design. When not using as the dedicated INIT_DONE pin, and when this pin is not used as an I/O pin, then connect this pin as defined in the Quartus II software. | Verify Guidelines have been met or list required actions for compliance. |
| CLKUSR |  | Optional user-supplied clock input which synchronizes the initialization of one or more devices. If not enabled as user-supplied configuration clock, it can be used as a user I/O pin. If the CLKUSR pin is not used as a configuration clock input and the pin is not used as an I/O then it is recommended to connect this pin to ground. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| JTAG Header |  | Power the EthernetBlaster II, ByteBlaster II or USB-Blaster cable’s VCC (pin 4 of the header) with VCCPD. For multi-device JTAG chains with different VCCIO voltages, voltage translators may be required to meet the I/O voltages for the devices in the chain and JTAG header. The EthernetBlaster II, ByteBlaster II and USB-Blaster cables do not support a target supply voltage of 1.2 V. For the target supply voltage value, refer to the EthernetBlaster II Communications Cable User Guide, ByteBlaster II Download Cable User Guide and the USB-Blaster Download Cable User Guide. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

Reviewed against Errata Sheet for Stratix V Devices (PDF) version:

Additional Comments:

Index  Top of Section

Section III: Transceiver

(Skip this section for Stratix V E devices)

Stratix V Recommended Reference Literature/Tool List

Stratix V Pin Out Files

Stratix V E, GS, GX Device Family Pin Connection Guidelines (PDF)

Stratix V Early Power Estimator

Stratix V Early Power Estimator User Guide (PDF)

Power Delivery Network (PDN) Tool For Stratix V Devices

Device-Specific Power Delivery Network (PDN) Tool User Guide (PDF)

Altera Board Design Resource Center (General board design guidelines, PDN design, isolation, tools, and more)

AN 583: Designing Power Isolation Filters with Ferrite Beads for Altera FPGAs (PDF)

AN 597: Getting Started Flow for Board Designs (PDF)

AN644: Migration Between Stratix V GX and Stratix V GT Devices (PDF)

Stratix V Hard IP for PCI Express User Guide (PDF)

Errata Sheet and Guidelines for Stratix V ES Devices (PDF)

Errata Sheet for Stratix V Devices (PDF)

Known Stratix V Issues

Index

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCA_GXB[L,R][0:3] (not all pins are available in each device / package combination) |  | Analog power, TX driver, RX receiver, CDR, specific to the left (L) side or right (R) side of the device. Connect VCCA_GXB to a 2.5V or 3.0V linear or low noise switching regulator. Connect to 2.5V if ALL of these conditions are true: the data rate is ≤ 6.5Gbps no ATX PLL is used the DFE, AEQ, and EyeQ are not intended to be utilized internally at any time Connect to 3.0V if ANY of these conditions are true: the data rate is > 6.5Gbps ATX PLLs are used The DFE, AEQ, or EyeQ are intended to be utilized internally at any time Note: It is safe to connect VCCA_GXB to 3.0V regardless of data rate, ATX PLL use, and internal feature (DFE / AEQ / EyeQ) use. In this configuration VCCT_GXB and VCCR_GXB must both be 1.0V. If VCCA_GXB is 2.5V, then VCCT_GXB and VCCR_GXB must be equal to VCC. This power rail may be shared with VCCA_FPLL and VCCAUX. With a proper isolation filter these pins may be sourced from the same regulator as VCCIO, VCCPD and VCCPGM, when each of these power supplies requires 2.5V. VCCA_GXB may be shared with VCCA_GXB from multiple devices. Do not share VCCA_GXB with noisy supplies such as VCCIO, VCCPD, and VCCPGM unless filtering is provided such as a ferrite bead. Decoupling depends on the design decoupling requirements of the specific board design. | Verify Guidelines have been met or list required actions for compliance. See Notes (3-1) (3-2) (3-3) (3-4) (3-5) (3-7) |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCH_GXB[L,R][0:3] (not all pins are available in each device / package combination) |  | Analog power, block level TX buffers. Connect VCCH_GXB to a 1.5V linear or low noise switching regulator. These pins may be sourced from the same regulator as VCCPT, VCCD_FPLL and VCCBAT. Decoupling for these pins depends on the design decoupling requirements of the specific board design. | Verify Guidelines have been met or list required actions for compliance. See Notes (3-1) (3-2) (3-3) (3-4) (3-5) (3-7) |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCT_GXB[L,R][0:3] (not all pins are available in each device / package combination) |  | Analog power, transmitter, specific to the left (L) side or right (R) side of the device. Connect VCCT_GXB pins to a linear or low noise switching regulator. VCCT_GXB and VCCR_GXB are either set to: VCCT_GXB = VCC (0.85V or 0.9V) when VCCA_GXB is connected to 2.5V (see detail / reasons in the VCCA_GXB section) VCCT_GXB = 1.0V when VCCA_GXB is connected to 3.0V (see detail / reasons in the VCCA_GXB section) VCCT_GXB = 1.05V ± 20mV when data rate ≥ 10.3Gbps and DFE is used Note: It is safe to connect VCCT_GXB to 1.0V regardless of data rate, ATX PLL use, and internal feature (DFE / AEQ / EyeQ) use. In this configuration VCCR_GXB must also be 1.0V, and VCCA_GXB must be 3.0V. For data rates less than 6.5Gbps and with a proper isolation filter these pins may be tied to the same regulator as VCC, VCCHIP and VCCHSSI. In this configuration, VCCA_GXB must be 2.5V. For data rates less than 12.5Gbps these pins may share the same power rail as VCCR_GXB. However, for better performance VCCR_GXB and VCCT_GXB should be isolated by at least 60dB for a 1MHz to 100MHz bandwidth. For data rates greater than 12.5Gbps this power rail must be tied to its own power regulator. Decoupling for these pins depends on the design decoupling requirements of the specific board design. | Verify Guidelines have been met or list required actions for compliance. See Notes (3-1) (3-2) (3-3) (3-4) (3-5) (3-7) |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCR_GXB[L,R][0:3] (not all pins are available in each device / package combination) |  | Analog power, receiver, specific to the left (L) side or right (R) side of the device. Connect VCCR_GXB pins to a linear or low noise switching regulator. VCCT_GXB and VCCR_GXB are either set to: VCCR_GXB = VCC (0.85V or 0.9V) when VCCA_GXB is connected to 2.5V (see detail / reasons in the VCCA_GXB section) VCCR_GXB = 1.0V when VCCA_GXB is connected to 3.0V (see detail / reasons in the VCCA_GXB section) VCCR_GXB = 1.05V ± 20mV when data rate ≥ 10.3Gbps and DFE is used Note: It is safe to connect VCCR_GXB to 1.0V regardless of data rate, ATX PLL use, and internal feature (DFE / AEQ / EyeQ) use. In this configuration VCCT_GXB must also be 1.0V, and VCCA_GXB must be 3.0V. For data rates less than 6.5Gbps and with a proper isolation filter these pins may be tied to the same regulator as VCC, VCCHIP and VCCHSSI. In this configuration, VCCA_GXB must be 2.5V. For data rates less than 12.5Gbps these pins may share the same power rail as VCCT_GXB. However, for better performance VCCR_GXB and VCCT_GXB should be isolated by at least 60dB for a 1MHz to 100MHz bandwidth. For data rates greater than 12.5Gbps this power rail must be tied to its own power regulator. Decoupling for these pins depends on the design decoupling requirements of the specific board design. | Verify Guidelines have been met or list required actions for compliance. See Notes (3-1) (3-2) (3-3) (3-4) (3-5) (3-7) |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCHSSI_[L,R] |  | PCS power supply, specific to the left (L) side or right (R) side of the device. When used, all VCCHSSI pins require a 0.85V or 0.90V supply depending on core speed grade (-1/-2 = 0.90V, -3/-4 = 0.85V). These pins must be tied to the same 0.85V / 0.90V plane as VCC and VCCHIP. When not using any of the transceivers on one side of the device, VCCHSSI on that side of the device may be tied to GND. For data rates less than 6.5Gbps and with a proper isolation filter VCCR_GXB and VCCT_GXB may be sourced from the same regulator as VCC, VCCHIP and VCCHSSI. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (3-1) (3-2) (3-3) (3-7) |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| VCCHIP_[L,R] |  | PCIe Hard IP digital power supply, specific to the left (L) side or right (R) side of the device. When used, all VCCHIP pins require a 0.85V or 0.90V supply depending on core speed grade (-1/-2 = 0.90V, -3/-4 = 0.85V). These pins must be tied to the same 0.85V / 0.90V plane as VCC and VCCHSSI. When not using any of the HIPs on one side of the device, VCCHIP pins on that side of the device may be connected to GND. For data rates less than 6.5Gbps and with a proper isolation filter VCCR_GXB and VCCT_GXB may be sourced from the same regulator as VCC, VCCHIP and VCCHSSI. Decoupling for these pins depends on the design decoupling requirements of the specific board. | Verify Guidelines have been met or list required actions for compliance. See Notes (3-1) (3-2) (3-3) (3-7) |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| REFCLK_[L,R][0:11]p/n (not all pins are available in each device / package combination) |  | High speed differential reference clock positive and negative receiver channels, specific to the left (L) side or right (R) side of the device. These pins may be AC-coupled or DC-coupled when used. For the HCSL I/O standard, it only supports DC-coupling. In the PCI Express configuration, DC-coupling is allowed on the REFCLK if the selected REFCLK I/O standard is HCSL (High-Speed Current Steering Logic). Connect all unused REFCLKp and REFCLKn pins directly to GND. | Verify Guidelines have been met or list required actions for compliance. See Notes (3-6) |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments/ Issues |
| --- | --- | --- | --- |
| GXB_RX_[L,R][0:31]p/n GXB_REFCLK_[L,R][0:31]p/n (not all pins are available in each device / package combination) |  | High speed positive and negative differential receiver or differential reference clock channels. Specific to the left (L) side or right (R) side of the device These pins may be AC-coupled or DC-coupled when used. Connect all unused GXB_RXp / GXB_REFCLKn and GXB_RXn / GXB_REFCLKn pins directly to GND. For more information about pin connection guidelines for Stratix V GX board designs that are intended to migrate to the Stratix V GT device, refer to AN644: Migration Between Stratix V GX and Stratix V GT Devices (PDF). | Verify Guidelines have been met or list required actions for compliance. See Notes (3-6) |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments/ Issues |
| --- | --- | --- | --- |
| GXB_TX_[L,R][0:31]p/n (not all pins are available in each device / package combination) |  | High speed positive or negative differential transmitter channels. Specific to the left (L) side or right (R) side of the device. Leave all unused GXB_TX pins floating. For more information about pin connection guidelines for Stratix V GX board designs that are intended to migrate to the Stratix V GT device, refer to AN644: Migration Between Stratix V GX and Stratix V GT Devices (PDF). | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments/ Issues |
| --- | --- | --- | --- |
| RREF_[T,B][L,R] |  | Reference resistor for transceiver, specific to the left (L) side or right (R) side of the device. If any PLL, REFCLK pin, or transceiver channel on one side (left or right) of the device is used, you must connect each RREF pin on that side of the device to its own individual 1.80-kΩ +/- 1% resistor to GND. Otherwise, you may connect each RREF pin on that side of the device directly to GND. In the PCB layout, the trace from this pin to the resistor needs to be routed so that it avoids any aggressor signals. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| nPERST[L,R][0:1] (N/A in Stratix V E Devices) |  | Dedicated fundamental reset pin is only available when used in conjunction with PCIe HIP. One nPERST pin is used per PCIe HIP. When this pin is not used as the fundamental reset, this pin may be used as a user I/O pin. Connect this pin as defined in the Quartus II software. This pin may be driven by 3.3V regardless of the VCCIO voltage level of the bank without a level translator as long as the input signal meets the LVTTL Vih/Vil specification, and as long as it meets the overshoot specifications for 100% operation as defined in Table 2-2 in DC and Switching Characteristics for Stratix V Devices (PDF). The Stratix V devices will always have all four nPERST pins listed, even when the specific device might have only one or two PCIe HIPs. nPERSTL0 = Bottom left PCIe HIP and CvP nPERSTL1 = Top left PCIe HIP (when available) nPERSTR0 = Bottom right PCIe HIP (when available) nPERSTR1 = Top right PCIe Hip (when available) The bottom left PCIe HIP should always be used first, this is the only PCIe HIP that supports CvP (Configuration Via Protocol - over the PCIe link). When using the bottom left PCIe HIP, connect nPERST from the PCIe slot directly to nPERSTL0. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

Notes:

3-1. Capacitance values for the power supply should be selected after consideration of the amount of power they need to supply over the frequency of operation of the particular circuit being decoupled. A target impedance for the power plane should be calculated based on current draw and voltage droop requirements of the device/supply. The power plane should then be decoupled using the appropriate number of capacitors. On-board capacitors do not decouple higher than 100 MHz due to “Equivalent Series Inductance” of the mounting of the packages. Proper board design techniques such as interplane capacitance with low inductance should be considered for higher frequency decoupling.  To assist in decoupling analysis, Altera's Power Delivery Network (PDN) Tool for Stratix V Devices serves as an excellent decoupling analysis tool.

3-2. Use the Early Power Estimation Tools to determine the current requirements for VCC and other power supplies.  Power pins should not share breakout vias from the BGA. Each ball on the BGA needs to have its own dedicated breakout via.

3-3. These supplies may share power planes across multiple Stratix V devices.

3-4. Low Noise Switching Regulator - defined as a switching regulator circuit encapsulated in a thin surface mount package containing the switch controller, power FETs, inductor, and other support components. The switching frequency is usually between 800kHz and 1MHz and has fast transient response. The switching range is not an Altera requirement.  However, Altera does require the Line Regulation and Load Regulation meet the following specifications:

- Line Regulation < 0.4%.

- Load Regulation < 1.2%.

3-5. If any transceiver channels on the left or right side of the device are used, you must supply power to all the transceiver power pins on that side, respectively. If none of the transceiver channels are used on either the left side or right side, you may power down the unused side by connecting all the transceiver power pins on the unused side to GND. Transceiver power pins include VCCR_GXB, VCCT_GXB, VCCH_GXB, and VCCA_GXB. In the case where these power rails are tied to GND, they must all be tied to the same GND plane.

3-6. For AC-coupled links, the AC-coupling capacitor can be placed anywhere along the channel. PCI Express protocol requires the AC-coupling capacitor to be placed on the transmitter side of the interface that permits adapters to be plugged and unplugged.

3-7. Examples 1 - 3 and Figures 1 - 3 in the Stratix V E, GS, GX Device Family Pin Connection Guidelines (PDF) illustrate power supply sharing guidelines that are data rate dependent.

Index  Top of Section

Reviewed against Errata Sheet for Stratix V Devices (PDF) version:

Additional Comments:

Index  Top of Section

Section IV: I/O

Literature: Stratix V Devices

Stratix V Pin Out Files

Stratix V E, GS, GX Device Family Pin Connection Guidelines (PDF)

Altera Board Design Resource Center (General board design guidelines, PDN design, isolation, tools, and more)

Errata Sheet and Guidelines for Stratix V ES Devices (PDF)

Errata Sheet for Stratix V Devices (PDF)

Known Stratix V Issues

AN 597: Getting Started Flow for Board Designs (PDF)

Index

| Part A: Clock Pins |
| --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| CLK[0:27]p (not all pins are available in each device / package combination) |  | Multi-purpose pins with the following functionality: - Dedicated high speed positive differential clock or differential data input with OCT Rd support. - Single ended clock or data input with OCT Rt support. - Single ended output with OCT Rs support. The programmable weak pull up resistor is available for single ended I/O usage. Use dedicated clock pins to drive clocks into the device. These pins can connect to the device PLLs using dedicated routing paths or global networks. Refer to Clock Networks and PLLs in Stratix V devices (PDF) for further information on dedicated routing of clock pins to PLLs. Unused pins can be tied to GND or left unconnected. If unconnected, use the Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| CLK[0:27]n (not all pins are available in each device / package combination) |  | Multi-purpose pins with the following functionality: - Dedicated high speed negative differential clock or differential data input with OCT Rd support. - Single ended clock or data input with OCT Rt support. - Single ended output with OCT Rs support. The programmable weak pull up resistor is available for single ended I/O usage. Use dedicated clock pins to drive clocks into the device. When used as single ended clock inputs, these pins can connect to the device PLLs using global networks. These pins do not have dedicated routing paths to the PLLs. Refer to Clock Networks and PLLs in Stratix V devices (PDF) for further information on dedicated routing of clock pins to PLLs. Unused pins can be tied to GND or left unconnected. If unconnected, use the Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| FPLL_[B,T][L,C,R]_ CLKOUT0, or FPLL_[B,T][L,C,R]_ CLKOUTp, or FPLL_[B,T][L,C,R]_ FB0 (not all pins are available in each device / package combination) |  | Dual purpose I/O pins that can be used as: Two single ended clock output pins, or One differential clock output pair, or Single ended external feedback input pin If not used for their dedicated PLL input or output functionality, these pins are available for regular single ended I/O usage, or as a differential transmitter. Unused pins can be tied to GND or left unconnected. If unconnected, use the Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| FPLL_[B,T][L,C,R]_ CLKOUT1, or FPLL_[B,T][L,C,R]_ CLKOUTn (not all pins are available in each device / package combination) |  |  |  |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| FPLL_[B,T][L,C,R]_ CLKOUT2, or FPLL_[B,T][L,C,R]_ FBp, or FPLL_[B,T][L,C,R]_ FB1 (not all pins are available in each device / package combination) |  | Dual purpose I/O pins that can be used as: Two single ended clock output pins, or One differential external feedback input pair, or Single ended external feedback input pin If not used for their dedicated PLL feedback input or output functionality, these pins are available for regular single ended I/O usage, or as a differential receiver. Unused pins can be tied to GND or left unconnected. If unconnected, use the Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |
| FPLL_[B,T][L,C,R]_ CLKOUT3, or FPLL_[B,T][L,C,R]_ FBn (not all pins are available in each device / package combination) |  |  |  |

Index  Top of Section

Additional Comments:

Index  Top of Section

| Part B: Dedicated and Dual Purpose Pins |
| --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| RZQ[#] (number of RZQ pins is device / package combination specific) |  | Calibrated on chip termination reference pins for I/O banks. The RZQ pins share the same VCCIO with the I/O bank where they are located. The external precision resistor must be connected to the designated pin within the bank. When using calibrated OCT tie these pins to GND through either a 240-Ω or 100-Ω resistor, depending on the desired OCT impedance. Refer to I/O Features in Stratix V Devices (PDF) for the OCT impedance options for the desired OCT scheme. If not required for its dedicated function, this pin can be used as a regular I/O pin. When not using RZQ# for the external precision resistor or as a regular I/O pin, it is recommended that the pin be connected to GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DNU |  | Do not connect to power or ground or any other signal; these pins must be left unconnected. | Verify Guidelines have been met or list required actions for compliance. |
| NC |  | Do not drive signals into these pins. When designing for device migration these pins may be connected to power, ground, or a signal trace depending on the pin assignment of the devices selected migration. However, if device migration is not a concern leave these pins unconnected. See Knowledge Database solution rd03132006_933. | Verify Guidelines have been met or list required actions for compliance. |
| TEMPDIODEp |  | Pins used in conjunction with the temperature-sensing diode inside the Stratix V device. TEMPDIODEp is the bias-high input, TEMPDIODEn is the bias-low input. If the temperature-sensing diode is not used with an external temperature sensing device, connect these pins to GND. Refer to Power Management in Stratix V Devices (PDF) for a list of external temperature sensing devices that are compatible with the temperature sensing diode. | Verify Guidelines have been met or list required actions for compliance. |
| TEMPDIODEn |  |  | Verify Guidelines have been met or list required actions for compliance. |

Additional Comments:

Index  Top of Section

| Part C: Dual Purpose Differential I/O pins |
| --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| DIFFIO_RX[T,B,L,R] [##]p, DIFFIO_RX[T,B,L,R] [##]n (Refer to the device Pin Table for number of channels based on device selected) |  | These are true LVDS receiver channels on row and column I/O banks. Pins with a "p" suffix carry the positive signal for the differential channel. Pins with an "n" suffix carry the negative signal for the differential channel. If not used for differential signaling, these pins are available as single ended user I/O pins. These pins do not have dedicated differential transmitters. True LVDS receivers support OCT Rd when VCCIO and VCCPD is 2.5V. Unused pins can be tied to GND or unconnected. If unconnected, use Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DIFFIO_TX[T,B,L,R] [##]p, DIFFIO_TX[T,B,L,R] [##]n (Refer to the device Pin Table for number of channels based on device selected) |  | These are true LVDS transmitter channels on row and column I/O banks. Pins with a "p" suffix carry the positive signal for the differential channel. Pins with an "n" suffix carry the negative signal for the differential channel. If not used for differential signaling, these pins are available as single ended user I/O pins. These pins do not have differential receivers. Unused pins can be tied to GND or unconnected. If unconnected, use Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DIFFOUT_[T,B,L,R] [##]p, DIFFOUT__[T,B,L,R] [##]n (Refer to the device Pin Table for number of channels based on device selected) |  | These are emulated LVDS output channels. All user I/Os, including I/Os with true LVDS input buffers, can be configured as emulated LVDS output buffers. Pins with a "p" suffix carry the positive signal for the differential channel. Pins with an "n" suffix carry the negative signal for the differential channel. If not used for differential signaling, these pins are available as single ended user I/O pins. Emulated LVDS transmitters require external resistor networks. Unused pins can be tied to GND or unconnected. If unconnected, use Quartus II software programmable options to internally bias these pins. They can be reserved as inputs tristate with weak pull up resistor enabled, or as outputs driving GND. | Verify Guidelines have been met or list required actions for compliance. See Note (4-1). |

Index  Top of Section

Notes:

4-1. Refer to Knowledge Database solution rd12102002_3281 for further information regarding the concerns when I/O pins are left floating with no internal or external bias.  Ensure there are no conflicts between the Quartus II software device wide default configuration for unused I/Os and the board level connection.  Altera recommends setting unused I/O pins on a project wide basis to behave as inputs tri-state with weak pull up resistor enabled.  Individual unused pins can be reserved with specific behavior such as output driving ground or as output driving VCC to comply with the PCB level connection.

Index  Top of Section

Reviewed against Errata Sheet for Stratix V Devices (PDF) version:

Additional Comments:

Index  Top of Section

Section V: External Memory Interfaces

Stratix V Literature

Stratix V Recommended Reference Literature/Tool List

Stratix V Pin Out Files

Stratix V E, GS, GX Device Family Pin Connection Guidelines (PDF)

Altera Board Design Resource Center (General board design guidelines, PDN design, isolation, tools, and more)

Errata Sheet and Guidelines for Stratix V ES Devices (PDF)

Errata Sheet for Stratix V Devices (PDF)

External Memory Interface Literature

External Memory Interfaces in Stratix V Devices (PDF)

Board Layout Guidelines (PDF)

Device and Pin Planning (PDF)

DDR, DDR2, DDR3, QDRII/+ SRAM, RLDRAMII Literature

ALTMEMPHY Design Tutorials (PDF)

UniPHY Design Tutorials (PDF)

Index

| Part A: DDR/2 Interface Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Data pins - DQ |  | Place it on DQ pins of the DQ/DQS group. The order of the DQ bits within a designated DQ group/bus is not important; however, use caution when making pin assignments if you plan on migrating to a different memory interface that has a different DQ bus width (e.g. migrating from x4 to x8). Analyze the available DQ pins across all pertinent DQS columns in the pin list. | Verify Guidelines have been met or list required actions for compliance. |
| Data strobe - DQS/DQSn |  | Differential DQS - Should be placed on corresponding DQS and DQSn pins of the DQ/DQS group. Single ended DQS – Connect the DQS pin to the DQS pin of the corresponding DQ/DQS group. | Verify Guidelines have been met or list required actions for compliance. |
| Data Mask DM |  | Place it on one of the DQ pins in the group. DM pins need to be part of the write DQS/DQ group. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| mem_clk[n:0] and mem_clk_n[n:0] |  | mem_clk should be placed on the same side as DQ/DQS pins. Single-ended DQS signaling Any DIFFOUT pins. Differential DQS signaling – Use any DIFFOUT, DIFFIO_RX or DIFFIO_TX pins for the mem_clk[n:0] and mem_clk_n[n:0] signals. (where n is greater than or equal to zero). | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| clock_source |  | Input clock pin to the DDR2 core PLL - Dedicated PLL clock input pin with direct (not using a global clock net) connection to the PLL and DLL required by the interface. | Verify Guidelines have been met or list required actions for compliance. |
| Address |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● mem_clk* pins. ● DQ, DQS, or DM pins. | Verify Guidelines have been met or list required actions for compliance. |
| Command |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● mem_clk* pins. ● DQ, DQS, or DM pins. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Reset |  | Dedicated clock input pin. (high fan-out signal) The reset pin can alternatively be generated internally. | Verify Guidelines have been met or list required actions for compliance. |
| RZQ |  | Used for the implementation of calibrated OCT for the memory interface pins. RZQ should be in any 1.8V VCCIO bank. Make sure that the VCCIO of your DDR2 interface bank and the VCCIO of the bank with RZQ pin match. If the RZQ pins are used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Additional Comments:

Index  Top of Section

| Part B: DDR/2 Termination Guidelines |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Memory clocks @ Memory |  | Memory clocks use Unidirectional class I termination. They are typically differentially terminated with an effective 100-Ω resistance. For DIMM no termination is required as termination is placed on the DIMM itself. | Verify Guidelines have been met or list required actions for compliance. See Note (5-1). |
| Memory clocks@ FPGA |  | Use series 50-Ω output termination without calibration on the FPGA side. | Verify Guidelines have been met or list required actions for compliance. See Note (5-1). |
| DQS @ Memory |  | Use ODT for DDR2. Use 50-Ω external parallel termination for DDR. | Verify Guidelines have been met or list required actions for compliance. See Note (5-1). |
| DQS @ FPGA |  | Use parallel 50-Ω with calibration as input termination. Use series 50-Ω with calibration as output termination. Source variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-1). |
| DQ @ Memory |  | Use ODT for DDR2. Use 50-Ω external parallel termination for DDR. | Verify Guidelines have been met or list required actions for compliance. See Note (5-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DQ @ FPGA |  | Use parallel 50-Ω with calibration as input termination. Use series 50-Ω with calibration as output termination. Source<variation_name>_pin_assignments.tcl file to assign these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-1). |
| DM@ Memory |  | Use ODT for DDR2. Use 50-Ω external parallel termination for DDR. | Verify Guidelines have been met or list required actions for compliance. See Note (5-1). |
| DM @ FPGA |  | Use series 50-Ω with calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-1). |
| Address [BA, mem_addr] @ Memory |  | Unidirectional class I termination. For multi-loads Altera recommends the ideal topology is a balanced symmetrical tree. Altera recommends that the class I termination to VTT is placed: ■ At the DIMM connector (for interfaces using DIMMs). ■ At the first split or division of the symmetrical tree for discrete devices. Nonsymmetrical topologies or DIMMs result in over or undershoot and oscillations on the line, which may require compensation capacitors or a lower than ideal drive strength to be specified resulting in de-rated interface performance. | Verify Guidelines have been met or list required actions for compliance. See Note (5-1). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Address [BA, mem_addr] @ FPGA |  | Use maximum current strength as the output drive strength. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically. | Verify Guidelines have been met or list required actions for compliance. |
| Command [CKE, CS_N, RAS, CAS, WE_N]@ Memory |  | Unidirectional class I termination. For multi-loads Altera recommends the ideal topology is a balanced symmetrical tree. Altera recommends that the class I termination to VTT is placed: ■ At the DIMM connector (for interfaces using DIMMs). ■ At the first split or division of the symmetrical tree for discrete devices. Nonsymmetrical topologies or DIMMs result in over or undershoot and oscillations on the line, which may require compensation capacitors or a lower than ideal drive strength to be specified resulting in de-rated interface performance. | Verify Guidelines have been met or list required actions for compliance. See Note (5-1). |
| Command [CKE, CS_N, RAS, CAS, WE_N]@ FPGA |  | Use maximum current strength as the output drive strength. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

5-1. The termination schemes suggested in the table are general guidelines. You should do board level simulation for your particular system/board to determine optimal termination scheme.

Index  Top of Section

| Miscellaneous |  |  |  |
| --- | --- | --- | --- |
| Pin Description | Schematic Name | Connection Guidelines | Comments/ Issues |
| Vref |  | Use voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. See Note (5-2). |
| Vtt |  | Use voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. See Note (5-2). |
| RZQ |  | RZQ pin is connected to GND through an external 240-Ω or 100-Ω ±1% resistor. Refer to I/O Features in Stratix V Devices (PDF) for the OCT impedance options for the desired OCT scheme. If the RZQ pin is used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

5-2. This worksheet does not calculate required decoupling, it is expected the designer will select decoupling based on analysis of power required and impedance of power path required based on static and switching current values.  Refer to Altera’s Power Delivery Network (PDN) Tool for Stratix V Devices for further information.

Capacitance values for the power supply should be selected after consideration of the amount of power they need to supply over the frequency of operation of the particular circuit being decoupled. A target impedance for the power plane should be calculated based on current draw and voltage drop requirements of the device/supply. The power plane should then be decoupled using the appropriate number of capacitors. On-board capacitors do not decouple higher than 100 MHz due to “Equivalent Series Inductance” of the mounting of the packages. Proper board design techniques such as interplane capacitance with low inductance should be considered for higher frequency decoupling.

Index  Top of Section

Additional Comments:

Index  Top of Section

| Part C: DDR3 Interface Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Data pin - DQ |  | Place it on DQ pins of the DQ/DQS group. The order of the DQ bits within a designated DQ group/bus is not important; however, use caution when making pin assignments if you plan on migrating to a different memory interface that has a different DQ bus width (e.g. migrating from x4 to x8). Analyze the available DQ pins across all pertinent DQS columns in the pin list. | Verify Guidelines have been met or list required actions for compliance. |
| Data strobe - DQS/DQSn |  | Should be placed on corresponding DQS and DQSn pins of the DQ/DQS group. | Verify Guidelines have been met or list required actions for compliance. See Note (5-3). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| mem_clk and mem_clk_n |  | The mem_clk signal should be placed on the same side as DQ/DQS pins. Devices (without leveling) – any unused pins with DIFFOUT, DIFFIO_TX,or DIFFIO_RX capability for the mem_clk[n:0] and mem_clk_n[n:0]signals (where n is greater than or equal to zero). Devices (with leveling) – you can assign the memory clocks to any unused DQ or DQS pins with DIFFOUT, DIFFIO_TX, or DIFFIO_RX capability for the mem_clk[n:0] and mem_clk_n[n:0] signals (where n is greater than or equal to zero). | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| clock_source |  | Input clock pin to the DDR2 core PLL - Dedicated PLL clock input pin with direct (not using a global clock net) connection to the PLL and DLL required by the interface. | Verify Guidelines have been met or list required actions for compliance. |
| DM |  | Data Mask Pin – Place it on one of the DQ pins in the group. DM pins need to be part of the write DQS/DQ group. | Verify Guidelines have been met or list required actions for compliance. |
| Address |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● mem_clk* pins. ● DQ, DQS, or DM pins. | Verify Guidelines have been met or list required actions for compliance. |
| Command |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● mem_clk* pins. ● DQ, DQS, or DM pins. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Reset for DDR3 Memory |  | Any user I/O pin. | Verify Guidelines have been met or list required actions for compliance. |
| Reset |  | Dedicated clock input pin. (high fan-out signal) The reset pin can alternatively be generated internally. | Verify Guidelines have been met or list required actions for compliance. |
| RZQ |  | Used when calibrated OCT for the memory interface pins is implemented. RZQ should be in any 1.5V VCCIO bank. Make sure that the VCCIO of your DDR3 interface bank and the VCCIO of the bank with RZQ pin match. If the RZQ pin is used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

5-3.  DDR3 only supports differential DQS signaling.

Index  Top of Section

Additional Comments:

Index  Top of Section

| Part D: DDR3 Interface Termination Guidelines |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Memory clocks@ Memory |  | Fly by termination scheme. Clock signals are already terminated on the DIMM. No need to put any termination on the board. Devices (without leveling) – differential termination resistor needs to be included in the design. Depending on your board stackup and layout requirements, you choose your differential termination resistor value. Devices (with leveling) – Fly by termination scheme. differential termination resistor needs to be included in the design. Depending on your board stackup and layout requirements, you choose your differential termination resistor value. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |
| Memory clocks@ FPGA |  | Use series 50-Ω output termination without calibration. Source <variation_name>_pin_assignments.tcl to make the setting. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |
| DQS @ Memory |  | Use ODT. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DQS @ FPGA |  | Set the option to use Dynamic OCT in the IP Toolbench. Use parallel 50-Ω with calibration as input termination. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |
| DQ @ Memory |  | Use ODT. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |
| DQ @ FPGA |  | Set the option to use Dynamic OCT in the IP Toolbench. Use parallel 50-Ω with calibration as input termination Source <variation_name>_pin_assignments.tcl file to assign these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |
| DM@ Memory |  | Use ODT. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |
| DM @ FPGA |  | Use series 50-Ω with calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Address [BA, mem_addr] @ Memory |  | DIMM - Fly by termination scheme. Address signals are already terminated on the DIMM. No need to put any termination on the board. Discrete Device (no leveling) - Unidirectional class I termination. Discrete Device (with leveling) – Fly by termination scheme. Terminated at the device. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |
| Address [BA, mem_addr] @ FPGA |  | Use maximum current drive strength. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |
| Command [CKE, CS_N, RAS, CAS, WE_N] @ Memory |  | DIMM implementation - Fly by termination scheme. Command signals are already terminated on the DIMM. No need to put any termination on the board. Discrete Device (no leveling) - Unidirectional class I termination. Discrete Device (with leveling) – Fly by termination scheme. Terminated at the device. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Reset for DDR3 Memory |  | Use SSTL-15 Class I I/O standard to meet the 1.5V CMOS logic levels on the DDR3 device or DIMM. It is not recommended to terminate this reset to Vtt. | Verify Guidelines have been met or list required actions for compliance. |
| Command [CKE, CS_N, RAS, CAS, WE_N] @ FPGA |  | Use maximum current drive strength. Source <variation_name>_pin_assignments.tcl file to make this assignment automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-4). |

Notes:

5-4. The termination schemes suggested in the table are general guidelines. You should do board level simulation for your particular system/board to determine optimal termination scheme.

Additional Comments:

Index  Top of Section

| Miscellaneous |  |  |  |
| --- | --- | --- | --- |
| Pin Description | Schematic Name | Connection Guidelines | Comments / Issues |
| Vref |  | Use a voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. |
| Vtt |  | Use a voltage regulator to generate this voltage. Typically DDR3 DIMMS have decoupling capacitors connected between VTT and VDD (1.5V) and it is recommended that designers follow this approach. | Verify Guidelines have been met or list required actions for compliance. |
| RZQ |  | RZQ pin is connected to GND through an external 240-Ω or 100-Ω ±1% resistor. Refer to I/O Features in Stratix V Devices (PDF) for the OCT impedance options for the desired OCT scheme. If the RZQ pin is used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Additional Comments:

Index  Top of Section

| Part E: QDR II/+ Interface Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Q – Read data pins |  | Assign it to the DQ pins of an available DQ/DQS pin group. The order of the DQ bits within a designated DQ group/bus is not important; however, use caution when making pin assignments if you plan on migrating to a different memory interface that has a different DQ bus width. Analyze the available DQ pins across all pertinent DQS columns in the pin list. | Verify Guidelines have been met or list required actions for compliance. |
| D – Write data pins |  | Assign it to the DQ pins of an available DQ/DQS pin group. The order of the DQ bits within a designated DQ group/bus is not important; however, use caution when making pin assignments if you plan on migrating to a different memory interface that has a different DQ bus width. Analyze the available DQ pins across all pertinent DQS columns in the pin list. | Verify Guidelines have been met or list required actions for compliance. |
| Read clock to the FPGA - CQ/CQn |  | CQ – Place it on CQ pin CQn – Place it on CQn pin of the corresponding group. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Write clock from the FPGA - K/Kn |  | K – Place it on DQS pin. Kn –Place it on DQSn pin. | Verify Guidelines have been met or list required actions for compliance. |
| Input clock for output data – C and Cn |  | Altera QDRII SRAM interface is implemented in single clock mode. Connect C and Cn high. Also, look for the connection guidance in the memory device datasheet. | Verify Guidelines have been met or list required actions for compliance. |
| QVLD |  | QVLD signal indicates that the read data coming to the FPGA is ready to be captured. Place it in the read DQS/DQ group. Only QDRII+ SRAM device has a QVLD pin. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| clock_source |  | Input clock pin to the QDRII/+ core PLL - Dedicated PLL clock input pin with direct (not using a global clock net) connection to the PLL and DLL required by the interface. | Verify Guidelines have been met or list required actions for compliance. |
| BWSn |  | Data Mask Pin – Place it on one of the DQ pins in the group. BWSn pins need to be part of the write DQS/DQ group. | Verify Guidelines have been met or list required actions for compliance. |
| Address |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● Clock pins. ● Data pins | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Command |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● Clock pins. ● Data pins | Verify Guidelines have been met or list required actions for compliance. |
| Reset |  | Dedicated clock input pin. (high fan-out signal). Reset signal can also be generated internally in your design. | Verify Guidelines have been met or list required actions for compliance. |
| d_off |  | Refer to memory specification and guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| RZQ |  | Used when calibrated OCT for the memory interface pins is implemented. RZQ should be in any 1.5V / 1.8V VCCIO bank. Make sure that the VCCIO of your QDRII interface bank and the VCCIO of the bank with the RZQ pin match. If the RZQ pin is used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Additional Comments:

Index  Top of Section

| Part F: QDRII/+ Termination Guidelines |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Write Clock (K/Kn) @ FPGA |  | Class I termination scheme. FPGA side termination is implemented through OCT feature so that no board level termination required on the FPGA side. For the write clock signals Altera recommends series OCT 50-Ω with calibration. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| Write Clock (K/Kn) @ Memory |  | Class I termination scheme. Write clock at the memory side should be terminated with class I Parallel termination at the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| Read Clock (CQ/CQn) @ FPGA |  | For the read clock signals Altera recommends using parallel OCT 50-Ω with calibration. If x36 emulated mode is being used, then it is recommended to terminate the split CQ/CQn clocks externally and not use the FPGA OCT. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Read Clock (CQ/CQn) @ Memory |  | Read clock output impedance is implemented with the help of ZQ input pin on the memory device side. If not, you need to put 50-Ω series OCT on the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| Write data - D @ FPGA |  | Use series 50-Ω with calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| Write data – D @ Memory |  | Write data at the memory side should be terminated with class I Parallel termination at the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Read data - Q @ FPGA |  | Use parallel 50-Ω with calibration as input termination. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| Read data - Q @ Memory |  | Read data output impedance is implemented with the help of ZQ input pin on the memory device side. If not, you need to put 50-Ω series OCT on the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| BWSn @ FPGA |  | Use series 50-Ω with calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| BWSn @ Memory |  | BWSn at the memory side should be terminated with class I Parallel termination at the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| QVLD @ FPGA |  | Use parallel 50-Ω with calibration as input termination. If x36 emulated mode is being used, then it is recommended to terminate the split on QVLD signal externally and not use the FPGA OCT. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Address @ FPGA |  | If there are multiple loads on certain FPGA output pins (for example, if the address bus is shared across many memory devices), use of maximum drive strength setting may be preferred over the series OCT setting. Use board level simulations to pick the optimal setting for best signal integrity. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| Address @ Memory |  | On the memory side, Altera recommends the use of external parallel termination on input signals to the memory. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| Command @ FPGA |  | If there are multiple loads on certain FPGA output pins (for example, if the address bus is shared across many memory devices), use of maximum drive strength setting may be preferred over the series OCT setting. Use board level simulations to pick the optimal setting for best signal integrity. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |
| Command @ Memory |  | On the memory side, Altera recommends the use of external parallel termination on input signals to the memory. | Verify Guidelines have been met or list required actions for compliance. See Note (5-5). |

Index  Top of Section

Miscellaneous:

| Pin Description | Schematic Name | Connection Guidelines | Comments/Issues |
| --- | --- | --- | --- |
| Vref |  | Use a voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. See Note (5-6). |
| Vtt |  | Use a voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. See Note (5-6). |
| RZQ |  | RZQ pin is connected to GND through an external 240-Ω or 100-Ω ±1% resistor. Refer to I/O Features in Stratix V Devices (PDF) for the OCT impedance options for the desired OCT scheme. If the RZQ pin is used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

Notes:

5-5. The termination schemes suggested in the table are general guidelines. You should do board level simulation for your particular system/board to determine optimal termination scheme.

5-6. This worksheet does not calculate required decoupling, it is expected the designer will select decoupling based on analysis of power required and impedance of power path required based on static and switching current values.  Refer to Altera’s Power Delivery Network (PDN) Tool for Stratix V Devices for further information.

Capacitance values for the power supply should be selected after consideration of the amount of power they need to supply over the frequency of operation of the particular circuit being decoupled. A target impedance for the power plane should be calculated based on current draw and voltage drop requirements of the device/supply. The power plane should then be decoupled using the appropriate number of capacitors. On-board capacitors do not decouple higher than 100 MHz due to “Equivalent Series Inductance” of the mounting of the packages. Proper board design techniques such as interplane capacitance with low inductance should be considered for higher frequency decoupling.

Index  Top of Section

| Part G: RLDRAM II/3 Interface Pins |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Data pin - DQ |  | Place it on DQ pins of the DQ/DQS group. The order of the DQ bits within a designated DQ group/bus is not important. | Verify Guidelines have been met or list required actions for compliance. |
| DM |  | Place on the DQ pins of the applicable DQ/DQS pin group. Refer to the “Exceptions for RLDRAM II and RLDRAM 3 Interfaces” Planning Pin and FPGA Resources (PDF) and the memory vendor’s RLDRAM II/3 component data sheet for further information. | Verify Guidelines have been met or list required actions for compliance. |
| QVLD |  | Place on a DQ pin in the same bank as the read data. Altera IP does not use the QVLD pin. You may leave this pin unconnected on your board. You may not be able to fit these pins in a DQS group. Refer to the “Exceptions for RLDRAM II and RLDRAM 3 Interfaces” Planning Pin and FPGA Resources (PDF) for further information. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Read clock to the FPGA - QK/QKn |  | Place on the corresponding DQS and DQSn pins of the DQ/DQS group. | Verify Guidelines have been met or list required actions for compliance. |
| Write clock from the FPGA - DK/DKn |  | Place on DQ pins in the same DQS group as the read data (Q) pins or in adjacent DQS group or in the same bank as the address and command pins. For more information, refer to “Exceptions for RLDRAM II and RLDRAM 3 Interfaces” in Planning Pin and FPGA Resources (PDF). DK/DK# must use differential output-capable pins. For a Nios-based sequencer configuration, the DK pins must be in a DQ group but the DK pins do not have to be in the same group as the data or QK pins. | Verify Guidelines have been met or list required actions for compliance. |
| Memory clock – CK/CKn |  | Place on any unused DQ or DQS pins with DIFFOUT capability. Place the memory clock pins either in the same bank as the DK or DK# pins to improve DK versus CK timing, or in the same bank as the address and command pins to improve address command timing. Do not place CK and CK# pins in the same DQ group as any other DQ or DQS pins. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| clock_source |  | Input clock pin to the RLDRAM IP core PLL - Dedicated PLL clock input pin with direct (not using a global clock net) connection to the PLL and DLL required by the interface. | Verify Guidelines have been met or list required actions for compliance. |
| Address A, BA |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● CK/CK# pins. ● DQ, DQS and DM pins. | Verify Guidelines have been met or list required actions for compliance. |
| Command CS#, REF#, WE# |  | Any user I/O pin. To minimize skew, you should place address and command pins in the same bank or side of the device as the following pins: ● CK/CK# pins. ● DQ, DQS and DM pins. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Reset for RLDRAM Memory (RLDRAM 3 only) |  | Any user I/O pin. | Verify Guidelines have been met or list required actions for compliance. |
| Reset |  | Dedicated clock input pin. (high fan-out signal) The reset pin can alternatively be generated internally. | Verify Guidelines have been met or list required actions for compliance. |
| RZQ |  | Used when calibrated OCT for the memory interface pins is implemented. RZQ should be in any IOBANK which has the same VCCIO as the VCCIO used for the RLDRAM II/3 IOBANKs. RLDRAM II : 1.5V or 1.8V. RLDRAM 3 : 1.2V Make sure that the VCCIO of your DDR3 interface bank and the VCCIO of the bank with RZQ pin match. If the RZQ pin is used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Index  Top of Section

Additional Comments:

Index  Top of Section

| Part H: RLDRAM II/ 3 Interface Termination Guidelines |  |  |  |
| --- | --- | --- | --- |
| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| Write Clock (DK/DKn) @ FPGA |  | Use series 50 ohm without calibration as output termination. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |
| Write Clock (DK/DKn) @ Memory |  | RLDRAM 3 : Use ODT RLDRAM II : Write clock should be terminated with a differential termination at the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |
| Read Clock (QK/QKn) @ FPGA |  | Use parallel 50 ohm with calibration as input termination. Source <variation_name>_pin_assignments.tcl file to make these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |
| Read Clock (QK/QKn) @ Memory |  | Read clock output impedance is implemented with the help of the RLDRAM II /3 component ZQ input pin on the memory device side. If not, you may need to put 50-Ω series termination on the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Memory clocks @ Memory |  | Use a differential termination. Depending on your board stackup and layout requirements, choose your differential termination resistor value. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |
| Memory clocks @ FPGA |  | Use series 50-Ω output termination without calibration. Source <variation_name>_pin_assignments.tcl to make the setting. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |
| DQ @ Memory |  | Use ODT. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |
| DQ @ FPGA |  | Use Dynamic OCT which is parallel 50-Ω with calibration as input termination and series 50-Ω as output termination. Source <variation_name>_pin_assignments.tcl file to assign these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| DM @ Memory |  | Use ODT. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |
| DM @ FPGA |  | Use series 50-Ω as output termination. Source <variation_name>_pin_assignments.tcl file to assign these assignments automatically. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |
| QVLD @ Memory |  | Read clock output impedance is implemented with the help of the RLDRAM II /3 component ZQ input pin on the memory device side. If not, you may need to put 50-Ω series termination on the memory side. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |
| QVLD @ FPGA |  | If connected, use parallel 50-Ω with calibration as input termination. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Address [BA, mem_addr] @ Memory |  | Parallel termination to VTT is recommended. Micron technical noteTN-44-01 (RLDRAM 3 Design Guide) indicates that it may be possible to achieve adequate signal integrity without signal terminations at lower frequencies and with short PCB traces. Simulations should be performed to determine the termination requirements. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |
| Address [BA, mem_addr] @ FPGA |  | If there are multiple loads on certain FPGA output pins (for example, if the address bus is shared across several memory devices), use of maximum drive strength setting may be preferred over the series OCT setting. Use board level simulations to pick the optimal setting for best signal integrity. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |
| Command [CS#,WE#, REF#] @ Memory |  | REF#, WE# : Parallel termination to VTT is recommended. . CS# : Use either parallel termination to VTT or a pullup to VDD. Refer to the memory vendor’s RLDRAM II/3 component data sheet for further information. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |

Index  Top of Section

| Plane/Signal | Schematic Name | Connection Guidelines | Comments / Issues |
| --- | --- | --- | --- |
| Command [CKE, CS_N, RAS, CAS, WE_N] @ FPGA |  | If there are multiple loads on certain FPGA output pins (for example, if the address bus is shared across several memory devices), use of maximum drive strength setting may be preferred over the series OCT setting. Use board level simulations to pick the optimal setting for best signal integrity. | Verify Guidelines have been met or list required actions for compliance. See Note (5-7). |
| Reset for RLDRAM Memory (RLDRAM 3 only) |  | Use SSTL-12 Class I I/O standard to meet the CMOS logic levels on the RLDRAM 3 device. Use a pull-down resistor to GND. Typical value is 10kΩ, but you should select a suitable value for your implementation. Refer to the memory vendor’s RLDRAM II/3 component data sheet for further information. | Verify Guidelines have been met or list required actions for compliance. |

Notes:

5-7. The termination schemes suggested in the table are general guidelines. You should do board level simulation for your particular system/board to determine optimal termination scheme.

Additional Comments:

Index  Top of Section

| Miscellaneous |  |  |  |
| --- | --- | --- | --- |
| Pin Description | Schematic Name | Connection Guidelines | Comments / Issues |
| Vref |  | Use a voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. |
| Vtt |  | Use a voltage regulator to generate this voltage. | Verify Guidelines have been met or list required actions for compliance. |
| RZQ |  | RZQ pin is connected to GND through an external 240-Ω or 100-Ω ±1% resistor. Refer to I/O Features in Stratix V Devices (PDF) for the OCT impedance options for the desired OCT scheme. If the RZQ pin is used for standard non external memory interfaces, refer to section “Dedicated and Dual purpose pins” for connection guidelines. | Verify Guidelines have been met or list required actions for compliance. |

Additional Comments:

Index  Top of Section

Reviewed against Errata Sheet for Stratix V Devices (PDF) version:

Additional Comments:

Index  Top of Section

Section VI: Document Revision History

| Revision | Changes Made | Date |
| --- | --- | --- |
| V3.2 | Updated note 3-5 to specify unused transceiver power pin connection guidelines apply to the entire side of the device, not per bank. | September 2013 |
| V3.1 | Updated unused REFCLKp and REFCLKn pin connection guidelines to state pins can be tied directly to GND, using 10k-Ω resistors is not necessary. Added reference documentation to Transceiver section. | May 2013 |
| V3.0 | Synchronized with the Stratix V E, GS, and GX Device Family Pin Connection Guidelines version 1.6. Removed RREF_[T,B][L,R] from VCCA_FPLL and VCCD_FPLL and created a new row in the power section to clarify the dependency of the fPLL operation on the RREF pin connection. Updated nIO_PULLUP connection guideline to state it must be connected to GND. Updated VCCPD connection guideline to specify support for VCCIO3E. Added clarification to low noise switching regulator notes in the power section and transceiver section. Added power supplies can be shared across multiple devices for VCC, VCCIO, VCCPD, VCCPGM, VCCHIP, VCCHSSI, and VCCA_GXB. Added RLDRAMII/3 section. Updated VCCA_GXB, VCCT_GXB and VCCR_GXB voltage supply recommendations per Pin Connection Guidelines v1.6. Updated REFCLK recommendations related to DC coupling. | March 2013 |
| V2.1 | Clarified transceiver unused GXB_RX inputs as dual-use to include GXB_REFCLK. Corrected the GXB_RX and GXB_TX maximum available channels as [0:31]. Updated guidelines for VCCA_FPLL, VCCD_FPLL, and RREF_[T,B][L,R] to clarify the dependency of the fPLL operation on the RREF pin connection. | October 2012 |
| V2.0 | Clarified voltage requirements on VCCT_GXB and VCCR_GXB. | June 2012 |
| V1.8 | Synchronized with the Stratix V E, GS, and GX Device Family Pin Connection Guidelines version 1.4. Updated resistor value for MSEL. Added multi-device clarification for INIT_DONE. Updated TEMPDIODEp/n connection guidelines. Moved nPERST from the configuration section to the transceiver section. | June 2012 |
| V1.7 | Updated VCCA_GXB, VCCT_GXB, and VCCR_GXB connection guidelines related to data rate, ATX PLL use, and internal feature (DFE / AEQ / EyeQ) use. | May 2012 |

| V1.6 | Updated VCC connection guidelines to include 0.9V requirements for -1 and -2 speed grades. Added links to Stratix V Errata Sheet. | April 2012 |
| --- | --- | --- |
| V1.5 | Updated connection guideline on CLK[0:27]n to indicate these pins drive PLLs over global resources when used as single ended clock inputs. | March 2012 |
| V1.4 | Updated title to include the Stratix V GS variant. Updated the FPLL output pin signal names and connection guidelines for clarity. Changed signal name CvPCIe_CONFDONE to CvP_CONFDONE. | March 2012 |
| V1.3 | Fixed links to the Stratix V ES Errata sheets | November 2011 |
| V1.2 | Added a mandatory comment in all sections for reviewers to identify Errata Sheet version and ES Device Guidelines version used for the review. | November 2011 |
| V1.1 | Update to RZQ connection guidelines in the External Memory Interface section. Updated unused pin connection guidelines for REFCLK and GXB_RX pins. | July 2011 |
| V1.0 | Initial release, based on the Stratix V GX and Stratix V E Device Family Pin Connection Guidelines version 1.2. | June 2011 |

Index